## Slide 1: SorpPropLib: Development of a C-Wrapper
Mirko Engelpracht
Institute of Technical Thermodynamics, RWTH Aachen University
10/01/2020

## Slide 2: How to use SorpPropLib in higher programming languages
Higher programming language, e.g. Python, Matlab, …
Language loades SorpPropLib
With SorpPropLib a working pair class can be created
Working pair class contains all functions of isotherm and isotherm coefficients for selected working pair
Inputs by user
Working pair: e.g. CO2 / Silicagel
Isotherm: e.g. Toth
Equation: e.g. w(p,T)
Values: e.g. p=250 Pa, T=300 K
JSON
Coefficients
Functions
SorpPropLib
Outputs
Because of defined inputs, output is the loading w in kg/kg for p = 250 Pa, T = 300 K, Toth isotherm and working pair CO2 / Silicagel
Included by DLL

## Slide 3: Workflow of the SorpPropLib
Organisation of the SorpPropLib:
  workingPair.c: Calculates equilibrium properties
  isotherm.c: Executes isotherm functions
      isotherm_toth.c
      …
  Refrigerant.c: Executes equation of states
    refrigerant_vapourPressure.c
    …
  test_X.c: Testers for all C-Codes
  makefile: Generates project for Windows
JSON
Coefficients
Functions
SorpPropLib

## Slide 4: Workflow of the SorpPropLib
Initialisation: Creates working pair struct
  Strings indicating the working pair, isotherm, …
  Coefficients for equations extracted from JSON-file
  Isotherm and refrigerant struct containing functions pointers that refer to isotherm functions or refrigerant functions
Usage: Wrapper for all isotherm functions
After usage: Delete working pair struct to free memory
JSON
Coefficients
Functions
SorpPropLib

## Slide 5: Structure of JSON-file
[{Refrigerant | Working pair},
{Refrigerant | Working pair},
…
{Refrigerant | Working pair}
]
{“k”: {“_as_”: “dum_sorbent”,
“_rf_”: “Name of refrigerant”,
“_st_”: “dum_subtype”},
“v”: {“_ep_”: {“Equation1”: {“_c_”: “Literature”, “_e_”: Name of equation”, “_p_”: {“Parameter1”: Value, “Parameter 2”: Value, …},
….},
“_r_”: “Name of refrigerant”,
“_s_”: “dum_sorbent”,
“_t_”: “dum_subtype”}
}
General organisation
Organisation of refrigerant and working pairs
Database is array and elements of array are refrigerant or working pair object

## Slide 6: Implemented refrigerants
Refrigerant | EoS for psat(T), dpsat(T)_dT | EoS for rhol(T), drhol(T)_dT
R-134a | X | X
CO2 | X | X
Methane | X | X
Water | X | X
Isobutane | X | X
Propane | X | X
R-410a | X | Missing
R-507a | X | Missing
Propylene | Missing | Missing

## Slide 7: Implemented working pairs
Refrigerant | MOF | Carbon | Zeolite | Silicagel
R-134a |  | maxsorb-iii acf-a-20 |  | 
CO2 |  | norit-rb1 | 5a 13x | X
Methane |  | norit-rb1 |  | 
Water |  |  | 5a 13x | X
Isobutane | cubtc |  |  | 
Propane | cubtc | maxsorb-iii |  | 
R-410a |  | maxsorb-iii |  | 
R-507a |  | acf-a-20 |  | 
Propylene | cubtc |  |  | 

## Slide 8: Implemented refrigerant and isotherm functions
Refrigerant functions are based on generalised equations:
  P_sat(T) and dp_sat(T)_dT: Vapour pressure and its derivative wrt temperature
  Rhol(T) and drho_l(T)_dT: Saturated liquid density and its derivative wrt temperature
Classical isotherms: Langmuir, Toth and Dual-Site-Sips
  w(p,T): Loading depending on pressure & temperature
  p(w,T): Pressure depending on loading & temperature
  T(p,w): Temperature depending on pressure & loading
  dw(p,T)_dp: Derivative of loading wrt pressure
  dw(p,T)_dT: Derivative of loading wrt temperature

## Slide 9: Implemented refrigerant and isotherm functions
Dubinin isotherms: Dubinin-Astakhov
  W(A,rho_l): Volumetric loading depending on adsorption potential & density
  A(W,rho_l): Adsorption potential depending on volumetric loading & density
  dW(A,rho_l)_dA: Derivative of volumetric loading wrt adsorption potential
  dA(W,rho_l)_dW: Derivative of adsorption potential wrt volumetric loading
  w(p,T,p_sat,rho_l): Loading depending on pressure, temperature, vapour pressure & density
  p(w,T,p_sat,rho_l): Pressure depending on loading, temperature, vapour pressure & density
  T(p,w,p_sat,rho_l): Temperature depending on pressure, loading, vapour pressure & density
  dw(p,T,p_sat,rho_l)_dp: Derivative of loading wrt pressure depending
  dw(p,T,p_sat,rho_l)_dT: Derivative of loading wrt temperature depending
  All functions of classical isotherm  Use internal refrigerant functions

## Slide 10: Possible extensions of SorpPropLib
4 cases possible to extend SorpPropLib:
  Case 1: refrigerant and isotherm exist
  Case 2: Isotherm does not exist
  Case 3: Refrigerant does not exist
  Case 4: Function for isotherm (e.g. dp(T,w)_dT) does not exist
Necessary changes for each case presented on next slides

## Slide 11: Case 1 – Add new coefficients for a working pair
Refrigerant and isotherm are already implemented  Only adding of new coefficients to JSON-file
Add entry for equation of working pair in JSON-File
Save coefficients (for units, see Equations.docx)
Save literature coefficients taken from

## Slide 12: Case 2 – Add new isotherm
Create header: isotherm_name.h
 Function prototypes and documentation of functions
Create source code: isotherm_name.c
 Source code of functions and documentation of functions
Write tester and change makefile: test_isotherm_name.c
 Tester executes all isotherm functions
Add selection for new isotherm in initialisation for isotherm struct: isotherm.c
Extend test model of isotherm structure by new isotherm: test_isotherm.c

## Slide 13: Case 3 – Add new refrigerant
Add entry for refrigerant (dummy_sorbent, dummy_subtype) in JSON-file
If approach for refrigerant functions already exists, only save coefficients of refrigerant functions (see Equations.docx) in JSON-file
If approach for refrigerant functions does not exist, add additionally source code:
 refrigerant_vapourPressure.h, *.c: Add functions and documentation
 refrigerant_saturatedLiquidDensity.h, *c: Add functions and documentation
 refrigerant.c : Add selection of new refrigerant functions in initialisation function
 Write testers for the refrigerant functions
 Extend test model of refrigerant struct by new functions: test_refrigerant.c

## Slide 14: Case 4 – Add new functions for isotherms
If possible, add new isotherm functions for all existing isotherms
If possible, test new isotherm function for all existing isotherms by extending the corresponding test models
Within isotherm.c  Add function pointers for new isotherm functions in isotherm struct  Set function pointers to correct isotherm functions during initialisation  If necessary, add function wrappers
Extend test_isotherm.c by new isotherm functions
Withing workingPair.c  Add function wrappers for new isotherm functions
Extend test_workingPair.c by new isotherm functions