## Slide 1: SorpPropLib: Workflow of the C-Wrapper
Mirko Engelpracht
Institute of Technical Thermodynamics, RWTH Aachen University
16/01/2020

## Slide 2: The SorpPropLib: What it is for!
Calculates equilibrium properties (e.g. pressure) of adsorption and absorption phenomena
Equations for equilibrium properties saved as C functions
Coefficients of equilibrium equations summarized in JSON database
If required by equilibrium equations, additional properties (e.g. vapor pressure) calculated
JSON
Coefficient
database
Correlation equations
SorpPropLib
1) Search coefficients for working pair and equation
Return coefficients and execute equation

## Slide 3: How to use the SorpPropLib?
Inputs by user
Working pair: e.g. CO2 / Silicagel
Isotherm: e.g. Toth
Equation: e.g. w(p,T)
Values: e.g. p=250 Pa, T=300 K
Output
Because of defined inputs, output is the loading w in kg/kg for p = 250 Pa, T = 300 K, and working pair CO2 / Silicagel expressed by Toth isotherm
Load-time DLL
JSON
Coefficient
database
Correlation equations
SorpPropLib
1) Search coefficients for working pair and equation
Return coefficients and execute equation
Program used by the user

## Slide 4: Workflow of the C wrapper
C does not support object-oriented programming
Desired program sequence of the C wrapper:
Initialization: Set up WorkingPair-struct
Usage: Call equilibrium functions that have pointer to WorkingPair-struct as additional argument
End of program: Delete WorkingPair-struct to free allocated memory
JSON
Coefficient
database
Correlation equations
SorpPropLib
1) Search coefficients for working pair and equation
Return coefficients and execute equation
Add object-oriented features by structs
Use pointer to struct as argument of functions

## Slide 5: Initialization: Layout of the WorkingPair-struct
Structure is set up during initialization and contains the following data:
  Strings indicating working pair, adsorption equation, absorption equation, …
  Arrays containing coefficients for equilibrium equations and refrigerant equations
  Sub-structs containing function pointers referring to equilibrium and refrigerant equations
    Adsorption-struct: Equilibrium equations for adsorption
    Absorption-struct: Equilibrium equations for absorption (does not exist yet)
    Refrigerant-struct: Equations for fluid properties
Coefficients selected from database once during initialization
Function pointers set to required equations once during initialization
For complete WorkingPair-struct, memory allocated during initialization

## Slide 6: Usage: Layout of the equilibrium equations
For the WorkingPair-struct created during initialization, a pointer exists that refers to address of memory that contains data of the WorkingPair-struct
Examples for equilibrium equations are:
  p_wT(double w, double T, void *workingPair)
   Returns p / (Pa) depending on w / (kg/kg) and T / (K)
  w_pT(double p, double T, void *workingPair)
   Returns w / (kg/kg) depending on p / (Pa) and T / (K)
Pointer referring to WorkingPair-struct is used by all equilibrium equations as argument!
Conventions for units:
Inputs: SI-units
Output: SI-units
Coefficients: SI-units
For all equations, analytical solutions are implemented when possible

## Slide 7: End of program: Layout of the WorkingPair-destructor
C does not free automatically allocated memory when closing the program
User must free allocated memory before closing the program
We free memory by calling destructor of WorkingPair-struct

## Slide 8: Workflow of the C wrapper: Data flow of user input
(1) WorkingPair *newWorkingPair(…)
Inputs by user are strings indicating:
Sorbent
Sub-type of sorbent
Refrigerant
Isotherm equation
Vapor pressure equation
Saturated liquid density equation
1
Initialization
Create WorkingPair-struct:
Save strings as attributes of struct
Read coefficients for equations from JSON
Set function pointers to isotherm equations, refrigerant equations, ...
JSON
Coefficient
database
(2) json_interface.c:
Loads JSON database  Searches database for working pair entry  Searches entry for equations
(3) json_interface.c:
For identified equations, return coefficients as arrays  Save arrays as attributes of WorkingPair-struct
Adsorption-struct
Refrigerant-struct
(4) adsorption.c & refrigerant.c:
Initialize corresponding structs  Search for isotherm and refrigerant equations  Save addresses of equations to function pointers of adsorption- and refrigerant struct
WorkingPair-struct
(5) WorkingPair-struct
2
Usage
User can call, for example, different adsorption equations depending on isotherm type by wrapper functions of WorkingPair-struct  Wrapper function calls internally correct equation by function pointers of Adsorption-struct:
(6) double w_pT(double p, double T, void* workingPair):
Adsorption-struct  Isotherm type  w_pT
Inputs by user are:
Pressure p in Pa
Temperature T in K
Pointer to WorkingPair-struct
3
End
Free allocated memory of WorkingPair-struct
(7) void delWorkingPair(void* workingPair)

## Slide 9: Workflow of the C wrapper: Directory structure
data
JSON files: *.json
incl
Header files: *.h
lib
External libraries: cJSON
Created libraries: *.lib and *.dll
obj
Objected files created during compilation: *.obj
src
Source files: *.c
test
Scripts to test all source files: *.exe
For adsorption: adsorption_*.h
For absorption: absorption_*.h
For refrigerant: refrigerant_*.h
For working pair: workingPair.h
For adsorption: adsorption_*.c
For absorption: absorption_*.c
For refrigerant: refrigerant_*.c
For working pair: workingPair.c
For testers: test_*.c
Makefile for MSVS-compiler to create easily DLL of C wrapper

## Slide 10: Structure of JSON database
[{Refrigerant | Working pair},
{Refrigerant | Working pair},
…
{Refrigerant | Working pair}
]
{“k”: {“_as_”: “dum_sorbent”,
“_rf_”: “Name of refrigerant”,
“_st_”: “dum_subtype”},
“v”: {“_ep_”: {“Equation1”: {“_c_”: “Literature”, “_e_”: Name of equation”, “_p_”: {“Parameter1”: Value, “Parameter 2”: Value, …},
….},
“_r_”: “Name of refrigerant”,
“_s_”: “dum_sorbent”,
“_t_”: “dum_subtype”}
}
General organisation
Organization of refrigerants and working pairs
Database is array and elements of array are refrigerant or working pair object

## Slide 11: Implemented refrigerants
Refrigerant | EoS for psat(T), dpsat(T)_dT | EoS for rhol(T), drhol(T)_dT
R-134a | X | X
CO2 | X | X
Methane | X | X
Water | X | X
Isobutane | X | X
Propane | X | X
R-410a | X | Missing
R-507a | X | Missing
Propylene | Missing | Missing

## Slide 12: Implemented working pairs
Refrigerant | MOF | Carbon | Zeolite | Silicagel
R-134a |  | maxsorb-iii acf-a-20 |  | 
CO2 |  | norit-rb1 | 5a 13x | X
Methane |  | norit-rb1 |  | 
Water |  |  | 5a 13x | X
Isobutane | cubtc |  |  | 
Propane | cubtc | maxsorb-iii |  | 
R-410a |  | maxsorb-iii |  | 
R-507a |  | acf-a-20 |  | 
Propylene | cubtc |  |  | 

## Slide 13: Implemented refrigerant and isotherm functions
Refrigerant functions are based on generalised equations:
  P_sat(T) and dp_sat(T)_dT: Vapour pressure and its derivative wrt temperature
  Rhol(T) and drho_l(T)_dT: Saturated liquid density and its derivative wrt temperature
Classical isotherms: Langmuir, Toth and Dual-Site-Sips
  w(p,T): Loading depending on pressure & temperature
  p(w,T): Pressure depending on loading & temperature
  T(p,w): Temperature depending on pressure & loading
  dw(p,T)_dp: Derivative of loading wrt pressure
  dw(p,T)_dT: Derivative of loading wrt temperature
  dp(w,T)_dw: Derivative of pressure wrt loading
  dp(w,T)_dT: Derivative of pressure wrt temperature

## Slide 14: Implemented refrigerant and isotherm functions
Dubinin isotherms: Dubinin-Astakhov
  W(A,rho_l): Volumetric loading depending on adsorption potential & liquid density
  A(W,rho_l): Adsorption potential depending on volumetric loading & liquid density
  dW(A,rho_l)_dA: Derivative of volumetric loading wrt adsorption potential
  dA(W,rho_l)_dW: Derivative of adsorption potential wrt volumetric loading
  w(p,T,p_sat,rho_l): Loading depending on pressure, temperature, vapor pressure & liquid density
  p(w,T,p_sat,rho_l): Pressure depending on loading, temperature, vapor pressure & liquid density
  T(p,w,p_sat,rho_l): Temperature depending on pressure, loading, vapor pressure & liquid density
  dw(p,T,p_sat,rho_l)_dp: Derivative of loading wrt pressure depending
  dw(p,T,p_sat,rho_l)_dT: Derivative of loading wrt temperature depending
  dp(w,T,p_sat,rho_l)_dw: Derivative of pressure wrt pressure loading
  dp(w,T,p_sat,rho_l)_dT: Derivative of pressure wrt temperature depending